## Slide 1: Detecting Life A power and amplitude threshold detector for fish calls in the Gulf of Mexico
Nicolas Jeffress
Marine Bioacoustics Laboratory
Marine Physical Laboratory Internship
Notes: Hi I am Nic Jeffress a rising junior at Rice University in Houston texas studying Mechanical engineering, and I am going to present to you on what I have been working on this summer as an MPL Intern. I am building a detector and classifier that will identify types of fish calls near the site of the bp oil spill.

## Slide 2: Outline
Deepwater Horizon and our Motivation for the project.
Background
Main project components: Detector, Image Processor, Classifier
Project Overview
Discussion of Spectrograms and Whitening
Concepts
Detailed Discussion of the Detector and its filters
The Detector
Next steps to advance this project
Next Steps

## Slide 3: Deep Water Horizon
By Unknown - US Coast Guard - 100421-G-XXXXL- Deepwater Horizon fire (Direct link), Public Domain
https://commons.wikimedia.org/w/index.php?curid=10089914
Richard Pallardy, Deepwater Horizon oil spill of 2010, Encyclopædia Britannica,
https://www.britannica.com/event/Deepwater-Horizon-oil-spill-of-2010
Background
Notes: 4.9 million barrels; largest spill in history of petroleum industry
Explosion: April 20, 2010
Capping: July 12, 2010
Stopped: Sept 17, 2010

## Slide 4: Acoustic recordings
High-frequency Acoustic Recording Package
Data collection: July 2010 – April 2016
90 m depth
~30 mi from DWH oil spill
Background
Notes: Main Pass
Explain Harp
Show Louisiana

## Slide 5: Motivation
Background
Cumulative hours per week
Percent effort per week
Notes: Not Logged
Checking for Presence
Grey Points

## Slide 6: Project Overview
Purpose
Classify the Images as a call type or noise.
Mechanism
Image plots
Mechanism
Convolutional Neural Network
Purpose
Turn start and end times from the detector into similarly sized spectrogram images
Mechanism
Use data chunking and filtering to assist in call identification
Detector
Purpose
Computationally search six years of acoustic data and identify potential marine life calls.
Image Processor
Classifier
Project Overview
Notes: Mention cnn
I am going to focus on the detector because that is what I have worked the most on

## Slide 7: What is a Detector?
Many different types of detectors
This Detector is a threshold detector
  Any time that the sound level is greater than a certain threshold sets off the detector
  Very important that the fish call is the loudest thing in the recording
Goal 90% accuracy of detecting logged calls
Concepts
Notes: Loud Noise Detector
Assuming the fish call is short enough relative to the duration of the audio segment that it doesn't’t have a big impact on the averages

## Slide 8: Original Data
The Detector
Notes: This is what our original data looks like, cant see the call in there
We need to do somethings to it to be able to see the call
But first I need to explain what a spectrogram is.

## Slide 9: What is a Spectrogram?
Frequency (Hz) | 9 | 4 | 4 | 6 | -13 | 20 | -14 | -17 | 12 | -12
 | -11 | -12 | -17 | -16 | 13 | 3 | -12 | 0 | -6 | -15
 | -8 | 29 | 14 | 21 | 6 | 2 | -1 | 6 | 2 | -2
 | 25 | 16 | -18 | 21 | 29 | 22 | 22 | 1 | -20 | -10
 | -19 | 5 | -17 | 16 | 13 | -16 | 20 | 13 | 30 | 4
Time (sec) |  |  |  |  |  |  |  |  |  | 
Frequency (Hz) | 9 | 4 | 4 | 6 | -13 | 20 | -14 | -17 | 12 | -12
 | -11 | -12 | -17 | -16 | 13 | 3 | -12 | 0 | -6 | -15
 | -8 | 29 | 14 | 21 | 6 | 2 | -1 | 6 | 2 | -2
 | 25 | 16 | -18 | 21 | 29 | 22 | 22 | 1 | -20 | -10
 | -19 | 5 | -17 | 16 | 13 | -16 | 20 | 13 | 30 | 4
Time (sec) |  |  |  |  |  |  |  |  |  | 
X axis = Time
Y axis = Frequency
Each cell = Energy
Each number corresponds to a color
*Values were randomly generated for this example
Concepts
Notes: Warmer colors are louder
Inside each cell is a number that describes the energy level (how loud the sound is)

## Slide 10
The Detector
Notes: Look here is a call

## Slide 11: Making a Welch Power Spectral Density Estimate
Frequency (Hz) | 9 | 4 | 4 | 6 | -13 | 20 | -14 | -17 | 12 | -12
 | -11 | -12 | -17 | -16 | 13 | 3 | -12 | 0 | -6 | -15
 | -8 | 29 | 14 | 21 | 6 | 2 | -1 | 6 | 2 | -2
 | 25 | 16 | -18 | 21 | 29 | 22 | 22 | 1 | -20 | -10
 | -19 | 5 | -17 | 16 | 13 | -16 | 20 | 13 | 30 | 4
Time (sec) |  |  |  |  |  |  |  |  |  | 
Frequency (Hz) | Average Energy
800 | -.1
600 | -7.3
400 | 6.9
200 | 8.8
0 | 4.9
Concepts
*Taking average across each row
Notes: A Method to evaluate noise levels at different frequencies
Important Assumption

## Slide 12
Notes: Frequencies are relative to fish calls explain the units
Look we see that the average sound energy is not the same across all frequencies
This is bad because we could be missing calls in the noise

## Slide 13: Whitening
9 | 4 | 4 | 6 | -13 | 20 | -14 | -17 | 12 | -12
-11 | -12 | -17 | -16 | 13 | 3 | -12 | 0 | -6 | -15
-8 | 29 | 14 | 21 | 6 | 2 | -1 | 6 | 2 | -2
25 | 16 | -18 | 21 | 29 | 22 | 22 | 1 | -20 | -10
-19 | 5 | -17 | 16 | 13 | -16 | 20 | 13 | 30 | 4
÷
Average Energy
-1
8.8
4.9
6.9
-7.3
Concepts
Notes: The way you can think about this is white light, “equally important”
Calls can stand out anywhere

## Slide 14: Whitened vs Original Spectrogram
The Detector
Notes: This is my data after it has been whitened

## Slide 15: Step 1: Whitened Data
The Detector
Notes: From now on check out max peak to noise ratio
Explain the orange line

## Slide 16: Step 2: Highpass Filter
The Detector
Notes: Naked eye look the same
Point out the highpass filter
Computationally cheap

## Slide 17: Step 3: Power Threshold Filter
The Detector
Notes: Looking at top 5% of energy levels
This is my first stage threshold filter

## Slide 18: Step 4: Amplitude Threshold Filter
The Detector
Notes: Popcorn metaphor
This is my second threshold filter

## Slide 19: Detector stats
The Detector
Type | Detected | Present in Log | Accuracy (%)
Beats | 4 | 17 | 23
Buzz | 51 | 83 | 61
Click Train | 316 | 321 | 98
Croak | 205 | 221 | 92
Downsweep | 11 | 19 | 58
Jet-Ski | 99 | 109 | 91
Pulse Train | 22 | 52 | 42
Total | 708 | 822 | 86
Can process 2 years of data in 24 hours
Notes: Can process a little over 2 years in 24 hours.

## Slide 20: The Good
Click Train 98%
Croak 92%
Jet-Ski 91%
Notes: Click train 98
Croak 92
Jetski 91

## Slide 21: The Bad
Buzz 61%
Downsweep 58%
Pulse Train 42%
Notes: Buzz 61
Downsweep 58
Pulse train 42

## Slide 22: The Ugly
Beats 23%
Notes: Beats 23

## Slide 23: Next Steps
Debug Classifier
Run Detector on all Data
Make images of detections so everything is ready to go by the time classifier is debugged
Next Steps

## Slide 24: Thanks
Ana Sirovic
Jigarkumar Patel
Katherine Cameron (KC)
Camille Pagniello
William Hodgkiss
Eric Orenstein
MPL internship – Beverly Kennedy, Eva Friedlander
Instrument deployment, recovery, and data processing: T. Christiansen, C. Garsha, R. Griswold, B. Hurley, J. Hurwitz, E. O’Neil, B. Thayer, and S. Wiggins.
Ryan Kastner and students in CSE 145 & CSE 237D: Chao (Jack) Li, Jiashen Wang, Jeremy Smith, Rochelle Manongdo, Luis Llobrera, Tiffany Huang
Based on work supported by the NRDA partners, and BP (Award #20105138) and CIMAGE and CIMAGE II (grants from BP/The Gulf of Mexico Research Initiative).